## Slide 1: Introduction to Fluid Power
Prof. Jari Vepsäläinen

## Slide 2
The world
Solids
Fluids
Consists mainly of…
FEM
CFD
From a mechanical engineering perspective
Physics: Statics, dynamics, thermodynamics,
kinematics, mechanics…
Data: capturing things we can’t explain with physics
Notes: As Engineergs, we want to understand the world. How does it behave so that we can design systems that elegant, reliable, esthetic and efficient

## Slide 3: Fluid Power Systems
Biological systems
Engineering systems

## Slide 4: Intended learning outcomes
After this session, the student can…
Understand the fundamental principles of fluid power
Identify hydraulic system and its components
Understand the working principles of hydraulic components
Identify fluid power applications

## Slide 5: Contents
What is Fluid Power?
Fluid Power Systems
Applications and Research

## Slide 6: 1. What is Fluid Power?

## Slide 7
Fluid Power
Liquid = Hydraulics
Gas = Pneumatics
Linear
Rotational
Notes: Gas is elastic and Liquid is stiff

## Slide 8
How it works?
Power transmission with fluid
Distribution of power
Generation
Use
Power = Pressure x Flow
Fin
Fout,1
Pressure
Fout,1

## Slide 9: No pressure – no motion
Pressure difference causes flow.
Without pressure, there is no flow.
Why this doesn’t work?
M
High pressure
Low pressure

## Slide 10
Hydraulic force conversion
Two cylinders
Same pressure, bigger area for lift
Higher force, lower speed
Power transmission

## Slide 11
System types
Hydrostatic system
Hydrodynamic system
Force mostly linked to pressure p
Force mostly linked to flow qV
F
F
h
p = ⍴gh

## Slide 12
Pressure affects perpendicularly
Pressure is the same everywhere in the same volume

## Slide 13
Absolute pressure
Based on Bernoulli’s equation
Gauge pressure
Units
SI Unit Pascal: 1 Pa = 1 N/m²
105 Pa = 1 bar (engineering unit)
Notes: Hydraulic oil density = 833.3 kg/m^3
h = 0.5 m (big cylinder)
g = 9.81
Rho*g*h = 4087.3365 pa = 0.04 bar
Atmospheric pressure 101,325 Pa = 1,01325 bar

## Slide 14
Flow
Laminar flow
  Smooth and streamlined, low internal resistance
Turbulent flow
  Chaotic and irregular -> Energy loss
Depends on
  Pipe size
  Fluid viscosity
  Speed

## Slide 15: 2. Fluid Power Systems

## Slide 16
System Components
Power source
  Electric motor or engine + pump​
Actuators to convey movement
  Cylinders and motors
Valves for logic & control
Fluid to convey power
  Oil or water​
Utilities
  Pressure accumulator, heat exchanger, filters, tank

## Slide 17
Energy losses
K.-E. Rydberg, "Energy Efficient Hydraulics – System Solutions for Minimizing Losses," in National Conference on Fluid Power, "Hydraulikdagar'15", Linköping, Sweden, 2015.
If idling is taken into account, average efficiency can drop to 20 %

## Slide 18
Basic Hydraulic system
mg
2. Control
M
3. Power
4. Utilities
1. Actuation

## Slide 19: “Powerpack”: eMotor/Engine + Pump

## Slide 20
Bent axis pump
Video (8 min)

## Slide 21
Pumps
http://www.designworldonline.com/a-quick-and-easy-guide-to-hydraulic-pump-technology-and-selection/#_
Notes: Gear pumps simple and cheap (200 €). Can be noisy. Gerotor pump is an improved version (ei kuvassa). Fixed displacement
Piston pump for high pressure. Good efficiency. Can be variable displacement. Axial version driven by an angled swash plate. Also radial piston pumps available.
Vane pumps are quiet. Can also be variable displacement.
Friction and leakage.
Generally:
    Gear type: pmax  17  25 MPa ηt  0,7  0,85
    Vane type: pmax  7  25 MPa ηt  0,8  0,9
    Piston type: pmax  16  45 MPa ηt  0,85  0,95
Displacements: Vk  1  1000 cm3/r
Motor types are basically the same.
https://www.youtube.com/watch?v=MdesnTOpkCM
https://www.youtube.com/watch?v=a00nMBsfdS0

## Slide 22
Pump equations
Produced flow rate
Required torque
Required power
n = Rotational speed [r/s]
Vr = Displacement [m3/r]
p = Pressure difference between inlet
and outlet [Pa]
qV = Flow rate [m3/s]
v = Volumetric efficiency []
hm = Hydromechanical efficiency []
t = Overall efficiency []
= v  hm
Ideal and real values for flow, torque and power
More torque and rotational speed  input power
needed because of
Friction (hydromechanical efficiency)
Leakages (volumetric efficiency)
than in ideal pumps

## Slide 23
Pump efficiency
v : volumetric efficiency (leaks)
hm : hydromechanical efficiency (flow and mechanical frictions)
t : overall efficiency

## Slide 24: Actuation: Rotational and Linear

## Slide 25
Motors
Often exactly the same structure as in a pump
Types
    Axial piston
      Bent axis
    Radial piston
    Gear
    Vane

## Slide 26
Motor equations
Flow rate in
Produced torque
Power in
n = rotational speed [r/s]
 = angular velocity [rad/s]
Vr = swept volume [m3/r]
T = load torque [Nm]
p = pressure difference between
in- and outlet [Pa]
qV = flow rate [m3/s]
v = volumetric efficiency []
hm = hydromechanical efficiency []
t = overall efficiency []
= v  hm
Efficiency is taken into account inversly compared to pumps

## Slide 27: Cylinder Types
Non-differential (symmetric) type:
Single acting
Single or Double acting
Differential type:
Plunger type:
Telescopic type:

## Slide 28
Cylinder equations
Flow rate
Force balance
Required power
A1 = piston area on the working chamber [m2]
A3 = piston area on the opposing chamber [m2]
v = piston speed [m/s]
F = external load force [N]
pout = pressure on the opposing chamber [Pa]
v = volumetric efficiency []
hm = hydromechanical efficiency []
t = overall efficiency []

## Slide 29
Cylinder size
D= 500 mm
@ 400 bar
7.7 MN
Lift 800 tons
AIRBUS A380 - Superjumbo
3 jacks
Cylinders made in Finland
Empty mass 277 000 kg
Notes: If piston diameter 0.5 m, produced force at 40 Mpa ~7854 kN which equal lifting 800 000 kg.
Made in Ikkala, Lohja, Finland.

## Slide 30: Control: Valves

## Slide 31
Directional Control Valves

## Slide 32
Other valves
    Presure Relief Valve (PRV)
    To protect from over pressure
    Usually connects the protected line to tank
    Necessary component in practice
    Check valve
    Block reverse flow direction
    Shuttle valve
    Choose the larger pressure level

## Slide 33: Check valve
A
B
One-way operation
mg
M

## Slide 34: Pressure Relief Valve (PRV)
mg
M
Notes: Think of it as a check valve that is really tightly wound.

## Slide 35: Shuttle valve
Pressure passes from higher pressure
Comparison between ports A and B

## Slide 36: Energy Storage: Pressure Accumulator

## Slide 37
Pressure Accumulator
    Energy storage
    Fluid compresses nitrogen gas
    Pressure depends on loading condition
Bladder
Membrane
Piston

## Slide 38: System Architectures: Throttling vs. Pump control

## Slide 39
Throttle control
”Traditional system”
Constant Flow
  Engine on one speed
  Fixed displacement pump
< 40 % efficiency
Easy to control
Linear movement
 cylinder
Rotary movement
 motor

## Slide 40
Pump Contro
Aka Electro-Hydraulic Actuation (EHA)
Electric motor controls the flow
  No need for control valves
> 80 % efficiency
Difficult to control with varying loads and speeds
Hermansson, R. (2021). Testing and simulation of energy efficiency of direct drive hydraulic system. Master’s thesis.

## Slide 41
Hydraulic fluids
Oil
    Good lubricant
    Environmental hazard
    Health risk
      Food industry
    Expensive
    Fire hazard
    Viscosity index
  Filtering
    Metal chips, water, air
Water
    Needs additives to lubricate
    ”Clean”
    Expensive components
    Can freeze
    Corrosion
      Stainless steel must be used (or even plastics for low pressures)

## Slide 42
Pros
High power/weight –ratio
Linear and rotational motion
Robust control
  Compliant if needed
  Overload prevention
Freedom of system layout
  Distributed power
Cons
Energy efficiency
  22 % on avg.
    New tech even over 80%
Characteristics of pressure medium
  Leaks
  Impurities
Fluid power systems

## Slide 43: 3. Applications and Research

## Slide 44
Workmachines
Harvester
Wheel loader
Excavator
Mining loader

## Slide 45
Boston dynamics: Atlas
28 hydraulic joints

## Slide 46
Telescopic crane

## Slide 47
Airplanes
Elevator, rudder​
Landing gear​
Brakes​
Cargo doors, stairs

## Slide 48
Hydraulic press
Forming sheets by pressing them​ into a mold with a huge force

## Slide 49
Hydraulic brakes
Notes: Anti-lock Braking system

## Slide 50
Emerging Technologies
Exoskeletons
Aging population
Wave Energy Converters
Climate crisis

## Slide 51
Pneumatics
Production Line automation
- fast actuation

## Slide 52
Soft grippers
Compliant grip
Usually coupled with force sensing or haptic sensing
Notes: https://www.youtube.com/watch?v=DeZ2-Y7l4ic

## Slide 53
Soft gripper

## Slide 54
Pneumatic muscles
Very light weigth
Inherently compliant
Biomimetic
Notes: https://www.semanticscholar.org/paper/A-Pneumatic-Biped-with-an-Artificial-System-Niiyama/6165ce0d28cdc28a64ca68aae82884e2130766d3

## Slide 55: Research focus: Non-Road Mobile Machinery
There is a need for electrification to reduce emissions and improve efficency. High power requires large batteries and motors. Challeges:
Cost
Weight
Space
Heat
Challenge: Industry is very conservative, hard to introduce new solutions

## Slide 56: Research Topics Breakdown
Non-Road Mobile Machines
System Design
Improved Performance
Increasing Longevity
Thermal Design
Waste Heat Utilization
Energy Recuperation
Vibration Damping
Predictive Maintenance
Optimizing Components
Managing Peak Loads
Phase Change Materials
Adsorption Materials
Cooling Dimensioning
Notes: Energy Recuperation
Juhon tutkimus hydrauliarkkitehtuureissa, jossa hyödynnetään kineettistä ja potentiaalienergiaa toisista aktuaattoreista. Hyvin riippuvianen työsyklistä
Tarvitaanko Improved Perfomance alle Alternative Powertrains? Ei varmaan tartte mainita
Optimizing Components
Downsizing – using smaller motors which are coupled for peak loads – Topias’s work
Hydrauliikka venttiililohkon suunnittelu tekoälyavusteisesti? DriveForward, jatkoa Tapio Lantelan työlle – Jaakim? Juho? Uusi tyyppi? Voisi mennä myös WP4.DF
- Optimoitu tilan ja flown kannalta
- 3D printing
Vibration Dampening
Active control - Oliver
Waste Heat Utilization
Paineakkututkimus: Nanothrust -> DriveForward
Kivin nykyinen tutkimus paineakkujen energiatehokkuuden parantamiseksi jatketaan NanoThrustissa. Ainakin Hydrollilla olisi tähän kiinnostusta, heidän omassa tutkimussuunnitelmmassaan tästä on mainittu. Hyvä jatkumo. Jyri Juhala aikanaan tätä tutki ja Juuso teki dipan, mutta enemmänkin nopeita testejä eikä tehtyy pitkää selkeetä tutkimusta.
Nanothrust reaktori
Anna-Kaisa, Gabe, Ali, Heikki
Managing Peak Loads
PCM – Ali (FCPT funding! 2 years?)

## Slide 57
Summary
Hydraulics is a power transmission method​
Pressure differences required to create flow
High forces and power from compact actuators​
Good efficiency actuators, often bad efficiency systems
Hydraulic system consists of​
Powerpack: eMotor/Engine + Pump​
Actuators: Cylinders and motors
Valves: Directional and Control
Sensors: pressure, flow, position, force, temperature​
Fluid: oil, water​
Utilities: Pressure accumulator, heat exchanger, filters, tank