## Slide 1: Measurement systems & Data acquisition
KON-C2004 Mechatronics Basics
12.11.2024 Raine Viitala & Panu Kiviluoma

## Slide 2
Mechatronic machine - subsystems
Sensors
Actuators
Signal
processing
Controller
Controlling
computer
User Interface
Affect and sense the physical world
Communication
(Bus, IoT, 5G)
Other systems and machines

## Slide 3: Philosophy of measurements
Measurement is always an estimate of the true value
  Nobody can find out the true value
The real value exists only on the computer screen (CAD, signal analysing etc.)
  In the real world all the objects, measured signals and physical magnitudes are erroneous

## Slide 4: Architecture of a measurement system
Sensor
Measurement Device
Signal Conditioning
Analog-to-Digital Converter
Software
Driver
Application
Visual C++/Basic
Arduino
Labview
Matlab
…
National Instruments
Measurement Computing
Data Translation etc.
Measurand
Voltage
Current
Charge
…
L
Conversion to another, typically electric physical quantity
Texas instruments
Bosch PLC
Arduino etc.

## Slide 5: Signals Come in Two Forms: Digital and Analog

## Slide 6: Signals
Voltage
  Standard ranges
    0…10V
    0…5V
    1…5V
    -5…+5V
    -10…+10V
  Easy and cheap, susceptible to disturbance
Current
  Standard ranges
    0…20mA
    4…20mA
  Better immunity to disturbance
Digital
  0 or 1
  0 or 5 V
  0 or 3.3 V
  Easy to process further
  The best immunity to disturbance
  “Computer proof”
Analog

## Slide 7: Analog Terminology
Level
  The instantaneous value of the signal at a given point in time
Shape
  The form that the analog signal takes, which often dictates further analysis that can be performed on the signal
Frequency
  The number of occurrences of a repeating event over time

## Slide 8: Linearity
nonlinearity
Calibration
curve
quantity
reading

## Slide 9: Analog to Digital
  Selection criteria
  Number of bits
    Resolution, quantization noise
  Sampling frequency
    Dictates the highest measurable frequency
  Input range
    0…1V, ±5V, …
  Number of channels
    Multichannel
    Sample and Hold / Multiplexer
8bit  2^8 = 256
16bit  2^16 = 65536
22bit  2^22 = 4194304

## Slide 10
Digitized signal
0
0,1
0,2
0,3
0,4
0,5
0,6
0,7
0,8
0,9
1,0
1
2
3
4
0
5
6
7
3bit  23 = 8 values
Aika (s)
1Hz sine: 10S/sec, 3bit
  AD conversion
Outputted “signal”
Time Value
0 4 (100)
0,1 6 (110)
0,2 7 (111)
0,3 7 (111)
0,4 6 (110)
0,5 4 (100)
0,6 2 (010)
0,7 0 (000)
0,8 0 (000)
0,9 1 (001)
1,0 3 (011)
…
Resolution?

## Slide 11
0
0,1
0,2
0,3
0,4
0,5
0,6
0,7
0,8
0,9
1,0
1
2
3
4
0
5
6
7
3bit  23 = 8
Aika (s)
1Hz sine: 10S/sec, 3bit
Range?

## Slide 12
0
0,1
0,2
0,3
0,4
0,5
0,6
0,7
0,8
0,9
1,0
1
2
3
4
0
5
6
7
3bit  23 = 8
Aika (s)
1Hz sine: 10S/sec, 3bit

## Slide 13: Sampling frequency
Sampling
Generated signal
!!??

## Slide 14: Effects of sampling rate vs. signal frequency
fs=1000 Hz fs=10 Hz
Aliased!

## Slide 15: How to Prevent Aliasing Nyquist Theorem
Frequency
  To accurately represent the frequency of your original signal…
    You must sample at greater than 2 times the maximum frequency component of your signal
Shape
  To accurately represent the shape of your original signal…
    You must sample between 5–10 times greater than the maximum frequency component of your signal .

## Slide 16: Common Signal Conditioning for Voltage Measurements

## Slide 17: Conditioning Signals
Signal conditioning improves a signal that is difficult for your DAQ device to measure
Signal conditioning is not always required
Noisy, Low-Level Signal
Filtered, Amplified Signal

## Slide 18: Amplification
Used on low-level signals
Maximizes use of analog-to-digital converter (ADC) range and increases accuracy
Increases signal-to-noise ratio (SNR)

## Slide 19: Attenuation
Decreases the input signal amplitude to fit within the range of the DAQ device
Necessary when input signal voltages are beyond the range of the DAQ device

## Slide 20: Filtering
Filters remove unwanted noise from a measured signal and block unwanted frequencies
Time
domain
Frequency
domain

## Slide 21: Low pass filter
Passband = low frequencies
Stopband = high frequencies
Cutoff frequency
    Amplitude -3 dB i.e. gain ~0.7
Example: RC filter
    1st order low pass filter
    Simple to implement, not very effective
    1 resistor, 1 capacitor
    Cut off frequency:
Notes: Low pass filter used to prevent aliasing and to reduce noice and disturbances above the desired frequency range. Also used for example in bass speakers.
Ideally constant gain of 1 from DC (0 Hz) to cutoff frequency.
Cutoff frequency is usually not a clear corner in the frequency response.

## Slide 24: Fourier transform
Decomposing a signal into its sinusoidal frequency components
Signal in time domain
Signal in frequency domain
Notes: Fourier transformation is a useful tool in signal processing.
Fourier transformation is a tranformation from time domain to frequency domain.
Fourier transformation can be used for filtering or compression. Filtering is easier to do in frequency domain than in time domain.
If the signal is not pure sine wave, it contains frequency components much higher than the main frequency. Thus for other than sine waves, the sampling rate must be much higher than the main frequency in order to record the shape of the curve.

## Slide 25: Frequency domain analysis
Can be done easily using for example Matlab built-in function fft()
FFT = Fast Fourier Transform
SUM
+
+
Time domain
Frequency domain
Frequency domain
Time domain
Notes: Vasemmalla aikatason jaksollisia aaltomuotoja, jotka ovat synkronissa telan pyörimisnopeuteen eli yhden kierroksen jaksonaikaan T
Vastaavat signaalit taajuustasossa
Edellisten signaalien summa aikatasossa
Summasignaali taajuustasossa
Käytännön signaalit edustavat summasignaalia kohinalla höystettynä, joten taajuusanalyysillä havaitaan, mistä komponenteista signaali muodostuu
Oheisessa kuvassa on käsitelty ainoastaan synkroniset taajuudet - taajuusanalyysin spektri kertoo kuitenkin kaikki merkittävät harmooniset taajuuskomponentit - myös asynkroniset

## Slide 26: Fourier transform
Notes: Higher frequency components not necessarily smaller as in the animation.
Fourier Matlab demo.

## Slide 27: Discrete Fourier transform
Returns the amplitude of bands (or bins) of frequencies as complex numbers
    0 Hz = DC offset
    Magnitude = absolute value of complex number -> abs()
    Phase = angle of the complex number -> angle() or atan2()
FFT – Fast Fourier transform algorithm
    Matlab function fft(data)
Notes: FFT – Fast Fourier Transform is probably the most used algorithm in digital signal processing. Calculates the discrete Fourier transform.
Real part of the fft result presents the amplitude of the sine waves, complex part represents the phase shift between the sine waves.
Results are mirrored for certain mathematical reasons. Initially first cell is 0 Hz for the left side, in the middle are highest frequencies and last cell 0 Hz for the right side.. Matlab function fftshift can be used to rearrange the graph sot that 0 Hz in the middle.
FFT result does not have a physical unit associated with it. The frequencies of the bins are evenly distributed and have to be scaled to represent the real frequencies.

## Slide 28: Electromagnetic interference can ruin your measurements
Eliminate ground loops
Wire condition and quality
Coaxial
Twisted pair
Shielding (Eg. CAT 6)
Isolation
Galvanic
Inductive
optical

## Slide 29: Case: paper machine roll run-out
Dynamic run-out
  run-out as a function of the roll rotating frequency
Measurement objectives
  Measure run-out of the roll
  Measure angular velocity and angular position of the roll

## Slide 30: Run-out
-roundness
-bearing error
-bending of the roll
Notes: [6,59 3,26] [6,09 4,76][6,89 4,06 ][6,89 4,36][5,79 3,66][6,19 2,56][5,79 3,16][7,19 2,46][7,69 4,16][7,69 3,86][7,59 4,26][6,09 4,36]

## Slide 31: Architecture of a measurement system
Sensor
Measurement Device
Signal Conditioning
Analog-to-Digital Converter
Software
Driver
Application
Labview
DASYLab
Matlab
Visual C++/Basic
…
National Instruments
Measurement Computing
Data Translation
…
Measurand
Voltage
Current
Charge
…
L
Conversion to another, typically electric physical quantity

## Slide 32: Measurement setup
LPF
TTL
Sensors
Laser (displacement)
Filtering
LPF
Data acquisition
DAQ-card
Encoder (angle & speed)
Line receiver
Data processing and analysis
Labview
Matlab
DAQ
ENC
4 x LASER
PC
LabView
Matlab

## Slide 33: Sensors
Displacement (run-out)
Laser
Triangulation
Resolution 0.2μm
Sample rate 50kHz
Amplifier converts the distance to voltage: 1V ≡ 1mm

## Slide 34: Sensors
Angle (position and velocity)
encoder
Roll angle at each disp. value
1024 pulses/rev
  Resolution 0,35˚
Digital: 0V=0, 5V=1
2 channels + zero channel

## Slide 35: Measurement setup
LPF
TTL
Sensors
Laser (displacement)
Filtering
LPF
Data acquisition
DAQ-card
Encoder (angle & speed)
Data processing and analysis
Labview
Matlab
Line receiver
DAQ
ENC
4 x LASER
PC
LabView
Matlab

## Slide 36: Aliasing
Nyqvist: min. sample rate = 2x lowest frequency of the system
High frequency disturbance corrupts the data
LPF: let only the interesting frequencies to the DAQ-card

## Slide 37: Differential digital signal trasmission
Differential signal transmission
TTL receiver (digital signals)
Electromagnetic coupling based disturbance
  Variable frequency drive, electric motors, power supply units…

## Slide 38: Measurement setup
LPF
TTL
Sensors
Laser (displacement)
Filtering
LPF
Data acquisition
DAQ-card
Encoder (angle & speed)
Data processing and analysis
Labview
Matlab
Line receiver
DAQ
ENC
4 x LASER
PC
LabView
Matlab

## Slide 39: Data Acquisition
Measurement card – analog voltages and digital pulses are measured and converted to a computer-friendly format
NI USB-6215 USB
16 analog inputs (voltage, ±10V ), resolution 16 bit
2 analog outputs (voltage, ±10V), resolution 16 bit
4 digital inputs/outputs (0…5V)
Max. Sample rate 250 kHz
Multiplexer -> only one A/D-conversion unit ->converts voltages in turns from channel to channel

## Slide 40: Measurement setup
LPF
TTL
Sensors
Laser (displacement)
Filtering
LPF
Data acquisition
DAQ-card
Encoder (angle & speed)
Data processing and analysis
Labview
Matlab
Line receiver
DAQ
ENC
4 x LASER
PC
LabView
Matlab

## Slide 41: Measurement programming
Measurement task must be programmed to the DAQ-card
What is measured, which channel, how often…
Labview, Matlab, C++, arduino…

## Slide 42: Measurement setup
LPF
TTL
Sensors
Laser (displacement)
Filtering
LPF
Data acquisition
DAQ-card
Encoder (angle & speed)
Data processing and analysis
Labview
Matlab
Line receiver
DAQ
ENC
4 x LASER
PC
LabView
Matlab

## Slide 43: Analysis
From data to information
LabView, Matlab,…:
  Data usually in text or binary forms
  Data manipulation
  Averaging
  Frequency domain analysis (Fast Fourier Transform, FFT)
  Charts and graphs

## Slide 44: Analysis

## Slide 45: Measurement uncertainty
True value not reachable
  How to find out the error??? (measured – true value)
    Not possible!
  Measured values and Measurement uncertainty are both statistical variables: the result is within certain limits with certain probability
Systematic error -> calibration
  For example constant error in a meter
Random error -> uncertainty
  For example noise, vibration, stresses, temperature, measurer…
  Harder to control!

## Slide 46: Case: error sources – laser
Positioning error of the sensors (syst.)
Nonlinearity (syst.)
Noise and other EMC disturbance before DAQ
LPF
TTL
DAQ
ENC
4 X LASER

## Slide 47: Case: error sources - encoder
Angular positioning error (syst.):
LPF
TTL
DAQ
ENC
4 X LASER

## Slide 48: Case: error sources - measurer
Measurer causes easily systematic, random or coarse errors
Wrong
  parameters
  calibration
  position
  way of using a sensor
  …