## Slide 1: Other actuators
KON-C2004 Mechatronics Basics
Raine Viitala 19.11.2024

## Slide 2: Feedback
These exercies were really fun and interesting. The difficulty was on point in my opinion.
Exercises were ok but I didn't like the Fourier Analysis assignment. Got a mental breakdown from that one but I guess I learned something which was good.
This weeks exercise was great. I especially appreciated the fourier transform exercise, it gave me a greeat intuition for what the fourier transform does and why it is useful. P.S. can there be a whole course about only lithography and ASML machines? I volunteer as TA.
reliant on correct completion of last exercise
The exercise are amazing and great to solve them but would like more sessions so we can get the help needed.
👍good exercise
fun and enjoyable
Very difficult but still doable
More readable formating for the instructions, please. For example bullet points instead of wall of text.
This weeks exercises felt easier, i feel suspicious. Overall enjoyed the simulink exercise.
When do the hard exercises begin?
Sick

## Slide 3
Mechatronic machine - subsystems
Sensors
Actuators
Signal
processing
Controller
Controlling
computer
User Interface
Affect and sense the physical world
Communication
(Bus, IoT, 5G)
Other systems and machines

## Slide 4: Lecture overview & learning outcome
Pneumatics
Linear motion with electromagnetic devices
    Conversion from rotary motion
    Solenoid
    Voice coil
    Linear electric motors
Active materials
    Piezoelectric actuators
    Magnetorheological fluid
MEMS actuators
 Know the operating principle of multiple ”other actuators”

## Slide 5: Pneumatics

## Slide 6: Pneumatics
Cheap actuators
Moderate forces
Clean and safe
    Food industry
    Oil industry
Fast, repetitive motions
    Gripping, stamping, valve actuators etc.
Usually open loop because of compressibility
    Movements against a mechanical stop
    Servosystems also possible
Notes: Fluid power – transmission medium in pneumatics is gas, usually air. Same principles as in hydraulics.
High power to weight ratio (lighter than hydraulics)
No power required to maintain force or torque
Prices for non-repairable, rod-type cylinders range from $15 to $250 depending on body diameter, stroke and options.
Video: A slow amateur pneumatic pick&place example https://www.youtube.com/watch?v=vwGYwFsyCSE
  Pneumatic tools – jackhammer, impact wrench, nail gun

## Slide 7: Pneumatic example
Notes: https://www.youtube.com/watch?v=L8YGeeaNavE

## Slide 8: Air supply
Supply pressure
    Typical range 2-10 bars (0.2-1 MPa)
    Usually 6-7 bars
Components
    Air compressor
    Filter, dryer
    Storage tank
Low system efficiency
    Heat produced by the compressor
    Leaks in piping
Notes:   Running the air compressor is expensive. Consumes a lot of electricity.
  Air supply system: air compressor, air treatment(filters, dryers) and primary storage
  Combined gas law
  Compressor’s waste heat can sometimes be utilized for heating.
  80 % of energy used by a compressor turns to heat
  https://www.compressedairchallenge.org/library/articles/2010-09-CABP.pdf
  Running the air compressor is expensive
  Air supply system: air compressor, air treatment(filters, dryers) and primary storage
  Combined gas law 𝒑𝑽/𝑻=𝒌

## Slide 9: Pneumatic cylinders
Force = pressure * piston area
Single or double acting
Force usually < 10 kN
Stroke 1-3000 mm
Rodless
    Very long strokes
Telescope
    Long stroke, compact when retracted
http://www.mathworks.com/matlabcentral/fileexchange/screenshots/3366/original.jpg
http://en.wikipedia.org/wiki/Pneumatic_cylinder
Notes: ”Any” diameter or stroke.
Cylinders have stick-slip friction which can cause problems at slow speeds or with accurate positioning.
With or without internal feedback sensors or linear guides.
Festo and SMC largest pneumatics companies.
High Speed 16 Ton Pneumatic Power Press
520 components per minute https://www.youtube.com/watch?v=1fOsEUMZ1Lc about 1:00
16 mm demosylkka 7 barilla 140 N, 40 mm sylkkä 880 N. 10 kN -> 135 mm piston diameter.

## Slide 10: Pneumatic grippers
”Cylinder” grippers
    Clamps or tooling jaws
    ”Fingers”
Vacuum grippers
    Vacuum created with ejector
http://www.deltatecnix.com/plc_prog.htm

## Slide 11: Pneumatic rotary actuators
Motors
    Used a lot in hand-held tools
      Sanders, power wrenches, grinders etc.
    Starter motors for large electric or combustion motors
    Dental drill – rpm up to 400 000
Semi-rotary devices
    Vane type
    Rack and pinion type
Notes: Rack and pinion makes possible larger than 360 degrees rotation, vane is always limited to less than a full turn. Small friction.
Vane type has no backlash. Double vane limited to less than half turn but double torque.
Also actuators which combine linear and rotary movement, for example a cylinder which rotates at the end of its movement.

## Slide 12: Pneumatic muscles and bellows
Single acting
High force
Short stroke
Bellows
    Forces can be over 200 kN
    Short stroke <0,5 m
Muscles
    Maximum force up to a few kilonewtons
    Stroke ~25 % of nominal length
http://pneumatics-en.timmer-pneumatik.de/artikel/artbild/maxi/ZHO-SP2.jpg
http://www.boblan.de/pictures/FESTO-FluidicMuscleInflated.jpg
Notes: No wear or lubrication requirements, basically maintenance free
Muscles do not produce force at max displacement
Largest standard bellow from Parker has a diameter of 660 mm and with an 8 bar pressure generates 240 kN of force. Can lift 24 tons of mass. Max. Stroke 430 mm.
Bellows can be used for heavy lifting, brakes, clamping, generating, isolating or damping vibration,
Why are not used more?

## Slide 13: Pneumatic muscles
Notes: Muscles 3:02 -> 4:55
https://www.youtube.com/watch?v=NNNfn7ac-rY

## Slide 15: Linear motion with electric devices

## Slide 16: Converting rotation to linear movement: Screws
Lead screw
    Nut with internal thread
    Friction caused by sliding
      Not for continuous use
Ball screw
    Nut with grooves and ball bearings
      Larger size
    High force - minimal friction
    High accuracy
http://www.roton.com/page.aspx?id=28
Notes: Ball screw can be used for higher power transmission because there is minimal heating and wear caused by sliding surfaces, unlike in a lead screw.
Ball screws can usually be also back-driven because of their low internal friction. Lead screws can not.
Screws convert the rotation to linear force but in addition they require external linear quides.
Backlash can be eliminated with some preload, required in for example CNC machines where positioning tolerance is some micrometers

## Slide 17: Lead screw example
Notes: 800 mm/sec, 1G acceleration
https://www.youtube.com/watch?v=W6eORZDD1Dg

## Slide 18: Converting rotation to linear movement: Gears and belts
Rack & pinion
    Rack = linear gear
    Pinion = circular gear
Chain & sprocket
Belt
    Timing belt
    Flat belt
Cam
http://en.wikipedia.org/wiki/Cam
http://en.wikipedia.org/wiki/Rack_and_pinion
http://en.wikipedia.org/wiki/Roller_chain
http://www.pbclinear.com/Blog/How-to-Adjust-Belt-Tension-on-an-MT-Series-Actuator
Notes: Rack and pinion used for example in the steering mechanism of cars.
Cams are used in combustion engines as valve actuators
A belt needs more tension to stay on the pulleys than a chain.

## Slide 19: Example: Ultimaker 3D printer
Notes: Z axis (table up and down) with a stepper driven lead/ball screw.
X and y axis (moving the extruder horizontally) with two stepper driven timing belts.

## Slide 20: Electric linear actuator
http://www.iai-gmbh.de/en/press-and-media/press-information/press-informationen-newsreader/items/x-y-z-electric-cylinders-take-the-air-out-of-linear-motion.html
http://machinedesign.com/linear-motion/what-s-difference-between-pneumatic-hydraulic-and-electrical-actuators
Notes: ”Electric cylinder” etc.
Cheaper and more efficient than pneumatics especially when only a few actuators required and no pressurized air source is readily available.

## Slide 21: Solenoid
End to end linear movement
Larger movement -> smaller force
Single acting
    Other direction with a return spring or another solenoid
Often used as actuators for hydraulic and pneumatic valves
coil
Notes: Generated force is inversely exponentially proportional to movement length
Usually linear movement but also rotary solenoids are available.
Maximum elecromagnetic force generated by a solenoid on a very small movement corresponds to approximately 15 bar pressure on the plunger. For example 125 N for a 1 cm diameter round plunger.
Controlling a solenoid is usually done with on/off switch but more intelligent energy-saving control can also be used.
Controlled with current/voltage.

## Slide 22: Solenoid example

## Slide 23: Voice coil
High force - up to kilonewtons
Stroke up to a few centimeters
Low moving mass – high dynamics
Accurate position control
    with internal or external position feedback sensors
Used for example in speakers and hard disks
Permanent magnet and coil
Notes: Permanent magnet and coil. Either moving coil – stationary magnet or the other way around
Housed or without housing, internal or external position sensors
Controlled with current, reversing the current reverses the direction of the force. Force is proportional to current.
Simple construction, no gears. Completely silent and there is no backlash when direction is reversed ( “hysteresis free”). Voice coils naturally provide a force, specified by the current through the coil
A hard disk’s read and write head is positioned with a voice coil
Voice coil and solenoid both are used usually for small-scale applications.
Radially magnetized permanent magnets in the tube.

## Slide 24: Voice coil example
Notes: https://www.youtube.com/watch?v=BQJg7I-4620&list=PLi4swtEpsWmc-Vn79Bh5mrKsq3LORxrWY
https://www.youtube.com/watch?v=Wjb6nV3Ia9k&index=6&list=PLi4swtEpsWmc-Vn79Bh5mrKsq3LORxrWY

## Slide 25: Voice coil principle
Notes: https://www.youtube.com/watch?v=BQJg7I-4620

## Slide 26: Linear motors
Moving coils on a rail of magnets
High speed – up to 6 m/s
High accuracy
    Depending on feedback resolution
    No backlash
    Stiffness depends on driving current and control rate
High reliability
Moderate force
Expensive
Notes: Rotary - to - linear conversion mechanisms add inertia, friction, compliance, backlash, and wear.
The same types as in rotaring electric motors– induction, brushed and brushless DC, stepper.
Expensive due to low production volume and expensive magnets
Linear feedback encoder is also much more expensive than rotary encoder
A rotary servo motor with a ball screw is a cheaper but slower version.
Slider is called forcer.
Train propulsion (AC), railgun, Hyperloop
2D versions also available.
Tubular versions also.
https://www.youtube.com/watch?v=7QC9DgrLQ1I
http://www.rockwellautomation.com/global/anorad/products/linear-motors/comparison.page

## Slide 27: Linear motor principle

## Slide 28: Linear motor example
Notes: 2000 mm/s, acceleration 5G
https://www.youtube.com/watch?v=BhcZBr38Kmc

## Slide 29: Active materials

## Slide 30: Piezoelectric stack actuators
Very high force / size
    For example Ø10 mm actuator -> 1 kN
    Comparable to hydraulics
Very low displacement
    About 0,1 % of length – 1 µm per 1 mm
    Positioning resolution in nanometers
    Can be amplified -> reduced stiffness and dynamics
High dynamics
    Sub-millisecond response
    Frequencies up to 100 kHz
http://www.physikinstrumente.com/product-detail-page/p-604-202820.html
http://img.directindustry.com/images_di/photo-g/piezoelectric-actuators-linear-multilayer-13949-4710033.jpg
Notes: No moving parts no lubrication high realiability
Often require high voltage – 50-1000 V
Blocking force at zero displacement.
No force at maximum displacement
Are used for example in fuel injectors in combustion engines. Printer heads to eject minimal amounts of ink.
No moving parts -> no wear

## Slide 31: Piezoelectric benders
Larger movement
    Up to a millimeter
Low force
    Benders <2 N
    Ring benders <20 N
http://www.noliac.com/Actuators-7787.aspx
http://www.opli.net/img/magazine/eo/2012/news/bimorph_pc_pi.jpg
Notes: Size max a few centimeters.
Loudspeakers (piezo buzzers).

## Slide 32: Piezo example application: micro gripper
Handles small components
    10-500 µm
2 double benders and 2 stacks
6 degrees of freedom
10 strain gages for position feedback
http://autsys.aalto.fi/en/MicroNanoRoboticsResults
Notes: The piezoelectric actuators are controlled in closed loop to compensate the non-linearities of the actuators. The feedback of the local controller s is provided by 10 strain gauges that are glued on the piezoelectric actuators.
Double benders bend both vertically and horizontally.

## Slide 33: Piezoelectric motor
”Piezoelectric stepping motor”
    Small steps -> high precision
Also known as ultrasonic motor
    Stepping frequency >20 kHz
Used widely as camera autofocus motor
Rotating or linear
Low cost, compact, high force/size
http://en.wikipedia.org/wiki/Piezoelectric_motor#mediaviewer/File:Piezomotor_type_inchworm.gif
http://www.motioncontroltips.com/faq-what-are-piezo-elements-and-piezo-motors/
Notes: Nanometer precision possible.
High speed possible. For example 0.5 m/s.

## Slide 34: Miniature piezoelectric linear motor
Notes: Linear speed 10 mm/s or rotational 12 000 rpm
Linear force up to 5 Nm
Operates on 3.3 V.
http://www.newscaletech.com/technology/squiggle-motors.php
https://www.youtube.com/watch?v=oTrzNwjWCBo

## Slide 35: Magnetorheological (MR) fluid
Hydraulic fluid (oil) with iron particles
Magnetic field controls the yield stress (”viscosity”) of the fluid
Applied in semiactive dampers
http://www.gizmag.com/go/5752/
Notes: Applications especially in semiactive dampers. Audi TT.
Can also be used to actuators.
Also electrorheological fluids available.

## Slide 36: Other active materials
Magnetostrictive materials
    Change in magnetic field – 0.1-0.2 % strain in material
    High force
Electrostrictive materials
    Electric field
Shape memory alloys (SMA, memory metal)
    Change in temperature -> change in shape
(Ferro-) Magnetic shape memory alloys
    Change in magnetic field – up to 10 % change in dimensions
Notes: Magnetostrictive materials very similar to piezos but require exernal magnetic circuit to produce the magnetic field.
Shape memory alloy – temperature induced change in the crystal structure of the metal. Austenite – martensite change. Change speed of temperature limits the response time. Heating is quick by current and resistive losses but cooling is often slow.
https://en.wikipedia.org/wiki/Shape-memory_alloy
MSMA – change in magnetic field induces a change in the crystal structure of the metal. Austenite – martensite change. Good frequency response and high strain, up to 10 %. Possible problems with crackingof the material .

## Slide 37: MEMS actuators

## Slide 38: MEMS actuators
Electrostatic comb drive
    Displacement max few micrometers
Thermal actuators
https://www.mems.sandia.gov/about/actuators.html#ref4
http://compliantmechanisms.byu.edu/content/ introduction-microelectromechanical-systems-mems
Notes: Comb drive – electrostatic force between the plates of a capacitor. The plates must never touch each other. The force is proportional to the capacitance between the plates. The principle only works for very short distances.
Also piezoelectric and electromagnetic.
https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-777j-design-and-fabrication-of-microelectromechanical-devices-spring-2007/lecture-notes/07lecture21.pdf

## Slide 39: Comb drive
Notes: https://www.youtube.com/watch?v=oTrzNwjWCBo

## Slide 40: MEMS stepper with integrated position sensor
Notes: https://www.youtube.com/watch?v=32HXlchQgsw

## Slide 41: MEMS example: Digital micromirror device
Digital micromirror device (DMD)
    4k projector -> 8 million tiny rotatable mirrors
https://en.wikipedia.org/wiki/Digital_micromirror_device
Notes: Used in DLP projectors
A DMD chip has on its surface several hundred thousand (millions) microscopic mirrors arranged in a rectangular array which correspond to the pixels in the image to be displayed. The mirrors can be individually rotated ±10-12°, to an on or off state. In the on state, light from the projector bulb is reflected into the lens making the pixel appear bright on the screen. In the off state, the light is directed elsewhere (usually onto a heatsink), making the pixel appear dark.
The mirrors themselves are made out of aluminum and are around 16 micrometres across. Each one is mounted on a yoke which in turn is connected to two support posts by compliant torsion hinges. In this type of hinge, the axle is fixed at both ends and literally twists in the middle. Because of the small scale, hinge fatigue is not a problem
Two pairs of electrodes control the position of the mirror by electrostatic attraction. Each pair has one electrode on each side of the hinge, with one of the pairs positioned to act on the yoke and the other acting directly on the mirror. The majority of the time, equal bias charges are applied to both sides simultaneously. Instead of flipping to a central position as one might expect, this actually holds the mirror in its current position.
https://www.youtube.com/watch?v=NN1R3Sqimk8
https://www.youtube.com/watch?v=UcT0ZIcL2B4
https://www.youtube.com/watch?v=N4aUU3-PKQ4

## Slide 42: Summary
Pneumatics is widely used in factories
    Cheap, safe and robust
    Energy inefficient
Solenoid vs voice coil
Ball/lead screws vs linear motors
Active materials have their niche applications
MEMS open new possibilities
Notes: Interesting application
https://www.youtube.com/watch?v=c-c1l9r6kLw