## Slide 1: Introduction to Raspberry Pi
Ville Klar
Doctoral Candidate
Machine Design

## Slide 2: What is Raspberry Pi ?
Arguably the most popular single board computer (SBC)
  Easy to get started with because basically every problem is documented
Add a computer with a OS to practically anything
  NOTE: Do not expect it to perform as well as your laptop
Support for a vast array of peripherals (thanks to the Linux kernel)
  USB devices, networking, displays, cameras, audio etc.

## Slide 3: What can you do with a Pi? (not so cool)
https://www.raspberrypi.org/magpi/magic-mirror/
http://mymediaexperience.com/raspberry-pi-xbmc-with-raspbmc/
https://github.com/foosel/OctoPrint
https://vadelmapii.com/blogi/yllapida-omaa-dropbox-kloonia-raspberry-pilla-kayttaen-owncloudia
https://learn.adafruit.com/pigrrl-2/overview

## Slide 4: What can you do with a Pi? (cool)
https://hackaday.io/project/1279-ramanpi-raman-spectrometer
https://www.raspberrypi.org/blog/real-time-depth-perception-with-the-compute-module/
https://hackaday.io/project/1269-mashberry-beer-brewing-with-raspberry-pi
https://www.raspberrypi.org/magpi/fabscan-pi-project-3d-scanning-for-all/
http://www.zdnet.com/article/build-your-own-supercomputer-out-of-raspberry-pi-boards/

## Slide 5: Raspberry Pi models

## Slide 6: Raspberry Pi advantages and disadvantages
Cheap (price per performance)
Well documented
Availability
  Also in terms of add-ons (HATs)
Versatile
Compact (especially Zero)
Scary linux (learning required)
Not real time*
No ADC (easy to add though)
PWM possible but limited frequency
* It is possible to install a RTOS on the Pi

## Slide 7: Getting started
Install OS
Configure OS
Connect peripherals
Write software
Profit (?)

## Slide 8: OS options
with Pixel or Lite

## Slide 9: Installation process
Get SD card (micro on newer Pi’s)
Format to FAT32 (for example with SD card formatter)
Using NOOBS:
Download NOOBS (sd-cards with pre-installed NOOBS can purchased)
Unzip and copy all contents to SD card (takes a while)
Boot
Using a disk image writer:
Download the disk image (.img)
Write the disk image on the SD card (“hard drive”)
  Windows: Win32 disk image writer or Etcher
  MacOSX / Linux: Use dd (or image writer with GUI such as Etcher)
Boot

## Slide 10: Connections
Camera connector
Ethernet
4x USB 2.0
GPIO
Display connector
Micro USB for power (min. 5V/1A)
HDMI
3.5mm Audio/Video Jack
MicroSD-slot
(underneath)

## Slide 11: On first boot…
NOOBS installer has GUI (Raspbian recommended)
Boots into raspi-config (you can run it with “sudo raspi-config”)
Expand file system, change password and change keyboard layout, enable ssh etc.

## Slide 12: Terminal or Pixel
There are two options when booting: shell or Pixel desktop (graphical session)

## Slide 13: Connect to WLAN
In GUI:
Choose WiFi network and connect
Without GUI :
sudo iwlist wlan0 scan // scan for networks
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf // open wpa_supplicant configuration
Add this to the bottom of the file
network={
ssid=“aalto open"
proto=RSN
key_mgmt=NONE
}

## Slide 14: SSH
Secure shell = Easy way to remotely access a Pi
After connecting to a WLAN we need to find out the Pi’s ip address
  Type ‘ip a’ in a terminal output is something like this
If you don’t have a monitor connected you can try to nmap the ip
If the Pi connects to the same router between boots, DHCP should give it the same ip
  You can also configure a static IP
Local ip address

## Slide 15: SSH
When you have obtained the ip-address you can access the Pi with e.g. Putty
If you can’t be bothered with IP addresses
You can also use hostnames
(doesn’t work with aalto open)

## Slide 16: CLI / Shell commands
Command | Description
ls | List contents of current directory (folder)
cd | Change directory
mkdir | Creates a new directory (make directory)
sudo | Execute as super user (“admin” / root privileges)
cp | Copy (syntax is cp src dest)
mv | Move (syntax is mv src dest)
rm | Remove
./ | Dot-slash means execute
nano | Launch nano text editor
apt-get update | Update repository list (update list of links to software downloads)
apt-get install | Install a package
reboot | Reboots the system (run with sudo)
poweroff | Turns the Raspberry Pi off (run with sudo)

## Slide 17: CLI/ Shell tips
Use tab to make the terminal autocomplete
Up and down keys to browse command history
Ctrl+c to kill a process, Ctrl+z to stop a process
Ctrl+r to search command history
Use ‘exit’ to close a terminal window
Type ‘man’ before the command to see it’s manual
Github repositories can be cloned (copied) with ‘git clone’
You can also open an sftp connection to the Pi to view and edit files & folders

## Slide 18: Programming language options
Almost everything
  C, C++, Python2/3, Javascript (node), Ruby, Lisp, Rust…
Most projects are either C or Python

## Slide 19: GPIO Libraries
WiringPi (C and Python)
  Blink example : http://wiringpi.com/examples/blink/
RPIO (python2/3)
  PWM via DMA (up to 1µs resolution)
Bcm2835.h (C)
Pigpio (javascript / python/ C)

## Slide 20: Demo 1: Video streaming
Installation instructions: https://github.com/jacksonliam/mjpg-streamer
  Already installed in these Pi’s
Connect the Raspicam, make sure it is working with
raspistill -o cam.jpg
Run mjpeg-streamer with (first cd into ~/Software/mjpg-streamer/mjpg-streamer-experimental) :
export LD_LIBRARY_PATH=.
./mjpg_streamer -o "output_http.so -w ./www" -i "input_raspicam.so"
View the stream at http://localhost:8080 or with another computer (on the same network) at http://<IP-address-of-Pi>:8080
You can also use usb web cameras with mjpeg-streamer
There are many other options for streaming: clvc, gstreamer,
Use ctrl+c to kill the stream

## Slide 21: Demo 2: WiringPi
Open terminal
cd into ~/Software/WiringPi_Blink
Connect LED to gpio 29 and short lead to ground
  We should put a current limiting LED but we can break the rules
Run blink with sudo ./blink
Try changing the pin to 28 (in the code) and run make to compile

## Slide 22: Demo 3: Servo
Open terminal
cd into ~/Software/Python_Servo
Connect servo to gnd, 5V and GPIO 4
Run sudo pigpiod to start the gpio daemon
Run the python script with
python servo_demo.py
You can give another pin as an argument to the script e.g. python servo_demo.py 18
Try changing the speed of the servo

## Slide 23: Tips
For (prototype) web servers: Python Flask
For GUIs: Tkinter (Python) or Qt (C++) or Node.js+Express.js
If you need e.g. read analog voltages and control motors  consider combining an Arduino with a Raspberry Pi
(Raspberry Pi commands Arduino board via serial (USB))

## Slide 24: Links
Help videos (getting started)
Embedded Linux Wiki
Raspberry Pi Forums
Hackaday.io Raspberry Pi projects
Adafruit learning guides
Raspberry Pi subreddit